## Slide 1: CS 4730 Distributed Systems
Networking Overview / Primer
Revised 9/13/24

## Slide 2: Network Layer
Function:
  Route packets end-to-end on a network, through multiple hops
Key challenge:
  How to represent addresses
  How to route packets
    Scalability
    Convergence
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Routers, Revisited
How to connect multiple LANs?
LANs may be incompatible
  Ethernet, Wifi, etc…
Connected networks form an internetwork
  The Internet is the best-known example
Routers

## Slide 4: Structure of the Internet
Ad-hoc interconnection of networks
  No organized topology
  Vastly different technologies, link capacities
Packets travel end-to-end by hopping through networks
  Routers “peer” (connect) different networks
  Different packets may take different routes
Network 2
Network 1
Network 3
Network 4

## Slide 5: Internetworking Issues
Naming / Addressing
  How do you designate hosts?
Routing
  Must be scalable (i.e. a switched Internet won’t work)
Service Model
  What gets sent?
  How fast will it go?
  What happens if there are failures?
  Must deal with heterogeneity
    Remember, every network is different
Internet Service Model
Best-effort (i.e. things may break)
Store-and-forward datagram network
Lowest common denominator

## Slide 6: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 7: Possible Addressing Schemes
Flat
  e.g., each host is identified by a 48-bit MAC address
  Router needs an entry for every host in the world
    Too big
    Too hard to maintain (hosts come and go all the time)
Hierarchy
  Addresses broken down into segments
  Each segment has a different level of specificity

## Slide 8: Example: Telephone Numbers
1-617-373-2177
West Village H
Room 248
Very General
Very Specific
West Village G
Room 213
3278
Updates are Local

## Slide 9: Binary Hierarchy Example
1**
10*
11*
100
101
110
111
0**
00*
01*
000
001
010
011
Datagram, Destination = 101

## Slide 10: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g., 192.168.21.76
  Each number is a byte
  Stored in Big Endian (Network Byte) order
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31

## Slide 11: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
  Too slow: 4 * 10GE ports needs 176Gbps memory bandwidth
    DRAM is 1-6 Gbps, TCAM is faster but 400x more expensive than DRAM
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers

## Slide 12: IP Address Naming Hierarchy
Class-based hierarchy
First three bits of the IP address are the prefix
Each prefix denotes:
  Class of network
  Size of the network
  The “name” or prefix of the network
Classless Interdomain Routing (CIDR)
Original, Old School Method
Modern Method

## Slide 13: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24

## Slide 14: Two Level Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by network class

## Slide 15: Class Sizes
Class | Prefix Bits | Network Bits | Number of Classes | Hosts per Class
A | 1 | 7 | 27 – 2 = 126 (0 and 127 are reserved) | 224 – 2 = 16,777,214 (All 0 and all 1 are reserved)
B | 2 | 14 | 214 = 16,398 | 216 – 2 = 65,534 (All 0 and all 1 are reserved)
C | 3 | 21 | 221 = 2,097,512 | 28 – 2 = 254 (All 0 and all 1 are reserved)
 |  |  | Total: 2,114,036 | 
Too many network IDs
Too small to be useful
Way too big

## Slide 16: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables (this becomes an issue)
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:
Subnet Mask is 255.255.192.0

## Slide 17: Subnet Example
Extract subnetwork:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 11000000 00000000
Subnet Mask:
10110101 11011101 01000000 00000000
Result:
Extract host:
10110101 11011101 01010100 01110010
IP Address:
& ~(11111111 11111111 11000000 00000000)
Subnet Mask:
00000000 00000000 00010100 01110010
Result:
Extract network:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 00000000 00000000
Network Mask:
10110101 11011101 00000000 00000000
Result:
10 means this is a class B network
Class B uses 16 bits total for the network name
Subnet mask is 255.255.192.0

## Slide 18: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 19: Example Routing Table
Address Prefix | Subnet Mask | Prefix After Masking (in Binary) | Next Hop
0.0.0.0 | 0.0.0.0 | ******** ******** ******** ******** | Port 4
18.0.0.0 | 255.0.0.0 | 00010010 ******** ******** ******** | Port 2
128.42.0.0 | 255.255.0.0 | 10000000 00101010 ******** ******** | Port 3
128.42.128.0 | 255.255.128.0 | 10000000 00101010 1******* ******** | Port 5
128.42.222.0 | 255.255.255.0 | 10000000 00101010 11011110 ******** | Port 1
Question: 128.42.222.198 matches four rows
  Which router do we forward to?
Longest prefix matching
  Use the row with the longest number of 1’s in the mask
  This is the most specific match

## Slide 20: Subnetting Revisited
Question: does subnetting solve all the problems of class-based routing?
NO
Classes are still too coarse
  Class A can be subnetted, but only 126 available
    e.g., company w/ a Class A and subnets to multiple locations has only 1 routing table entry
  Class C is too small
  Class B is nice, but there are only 16,398 available
Routing tables are still too big
  2.1 million entries per router

## Slide 21: IP Address Naming Hierarchy
Class-based hierarchy
First three bits of the IP address are the prefix
Each prefix denotes:
  Class of network
  Size of the network
  The “name” or prefix of the network
Classless Interdomain Routing (CIDR)
Each network is assigned a bitmask
The bitmask separates the network “name” portion of the IP address from the host portion
Original, Old School Method
Modern Method

## Slide 22: Classless Inter Domain Routing
CIDR, pronounced ‘cider’
Key ideas:
  Get rid of IP classes
  Use bitmasks for all levels of routing
  Aggregation to minimize FIB (Forwarding Information Base)
Arbitrary split between network and host
  Specified as a bitmask or prefix length
  Example: Northeastern
    129.10.0.0 with netmask 255.255.0.0
    129.10.0.0 / 16

## Slide 23: Example CIDR Routing Table
Prefix | Netmask | Prefix After Masking (in Binary) | IP Address Range
207.46.0.0 | 19 | 11001111 00101110 000***** ******** | 207.46.0 – 31.*
207.46.32.0 | 19 | 11001111 00101110 001***** ******** | 207.46.32 – 63.*
207.46.64.0 | 19 | 11001111 00101110 010***** ******** | 207.46.64 – 95.*
207.46.128.0 | 18 | 11001111 00101110 10****** ******** | 207.46.128 – 191.*
207.46.192.0 | 18 | 11001111 00101110 11****** ******** | 207.46.192 – 255.*
Hole in the Routing Table: No coverage for 96 – 127
Missing entry: 207.46.96.0/19

## Slide 24: Aggregation with CIDR
Original use: aggregating class C ranges
One organization given contiguous class C ranges
  Example: Microsoft, 207.46.192.* – 207.46.255.*
  Represents 26 = 64 class C ranges
  Specified as CIDR address 207.46.192.0/18
11001111
CF
207
00101110
2E
46
11xxxxxx
C0
192
xxxxxxxx
00
0
Decimal
Hex
Binary
0
8
16
24
31
18 Bits Frozen By Netmask
14 Arbitrary Bits

## Slide 25: CIDR Aggregation Example
Prefix | Netmask | Prefix After Masking (in Binary) | Next Hop
207.46.0.0 | 19 | 11001111 00101110 000***** ******** | Port 1
207.46.32.0 | 19 | 11001111 00101110 001***** ******** | Port 1
207.46.64.0 | 18 | 11001111 00101110 01****** ******** | Port 1
207.46.128.0 | 18 | 11001111 00101110 10****** ******** | Port 2
207.46.192.0 | 18 | 11001111 00101110 11****** ******** | Port 3
Aggregation allows multiple routes to be compressed together to shrink the size of the routing table
207.46.0.0
18
11001111 00101110 00****** ********
Port 1
207.46.0.0
17
11001111 00101110 0******* ********
Port 1
Same length netmask
All bits match except for the last one
Same port

## Slide 26: Size of CIDR Routing Tables
From www.cidr-report.org
CIDR has kept IP routing table sizes in check
  Currently ~900,000 entries for a complete IP routing table
  Only required by backbone routers

## Slide 27: Takeaways
Hierarchical addressing is critical for scalability
  Not all routers need all information
  Limited number of routers need to know about changes
Non-uniform hierarchy useful for heterogeneous networks
  Class-based addressing is too course
  CIDR improves scalability and granularity
Implementation challenges
  Longest prefix matching is more difficult than schemes with no ambiguity

## Slide 28: How Do You Get IPs?
IP address ranges controlled by IANA
  Internet Assigned Number Authority
  Roots go back to 1972, ARPANET, UCLA
  Today, part of ICANN
IANA grants IPs to regional authorities
  ARIN (American Registry of Internet Numbers) may grant you a range of IPs
  You may then advertise routes to your new IP range
  There are now secondary markets, auctions, …

## Slide 29: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 30: IP Datagrams
IP Datagrams are like a letter
  Totally self-contained
  Include all necessary addressing information
  No advanced setup of connections or circuits
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 31: IP Header Fields: Word 1
Version: 4 for IPv4
Header Length: Number of 32-bit words (usually 5)
Type of Service: Priority information (unused)
Datagram Length: Length of header + data in bytes
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Limits packets to 65,535 bytes

## Slide 32: IP Header Fields: Word 3
Time to Live: decremented by each router
  Used to kill looping packets
Protocol: ID of encapsulated protocol
  6 = TCP, 17 = UDP
Checksum
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Used to implement trace route

## Slide 33: IP Header Fields: Word 4 and 5
Source and destination address
  In theory, must be globally unique
  In practice, this is often violated
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 34: Problem: Fragmentation
Problem: each network has its own Maximum Transmission Unit (MTU)
  DARPA principles: networks allowed to be heterogeneous
  Minimum MTU may not be known for a given path
IP Solution: fragmentation
  Split datagrams into pieces when MTU is reduced
  Reassemble original datagram at the receiver
MTU = 2000
MTU = 4000
MTU = 1500
Datagram
Dgram1
Dgram2
1
2
3
4

## Slide 35: IP Header Fields: Word 2
Identifier: a unique number for the original datagram
Flags: M flag, i.e. this is the last fragment
Offset: byte position of the first byte in the fragment
  Divided by 8
Version
HLen
TOS
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 36: Fragmentation Example
MTU = 2000
MTU = 4000
MTU = 1500
Data
Data
Data
IP Hdr
IP
IP
ID = 123 Length = 3820, M = 0
3800
20
Length = 1996, M = 1,
ID=123, Offset = 0
Length = 1844, M = 0,
ID = 123, Offset = 247
1976
20
1824
20
1976
+ 1824
= 3800
Why 247? Offset is the previous length divided by 8

## Slide 37: Fragmentation Example
MTU = 2000
MTU = 1500
Data
Data
IP
IP
Data
Data
IP
IP
Length = 1996, M = 1,
ID = 123, Offset = 0
Length = 1844, M = 0,
ID = 123, Offset = 247
1976
20
1824
20
20
20
1480
496
Length = 516, M = 1,
ID = 123, Offset = 185
Length = 1500, M = 1,
ID = 123, Offset = 0
Data
Data
IP
IP
20
20
1480
344
Length = 364, M = 0,
ID = 123, Offset = 432
Length = 1500, M = 1,
ID = 123, Offset = 247
1480
+ 496
= 1976

## Slide 38: IP Fragment Reassembly
Performed at destination
All fragments with matching IDs belong together
  Sort them by offset for reconstruction
M = 0 fragment gives us total data size
  364 – 20 + 432 * 8 = 3800
Challenges:
  Out-of-order fragments
  Missing fragments
  Duplicate fragments
  Overlapping fragments
Basically, memory management nightmare
Data
IP
20
1480
Data
IP
20
496
Length = 516, M = 1, ID = 123, Offset = 185
Length = 1500, M = 1, ID = 123, Offset = 0
Data
IP
20
1480
Data
IP
20
344
Length = 364, M = 0, ID = 123, Offset = 432
Length = 1500, M = 1, ID = 123, Offset = 247

## Slide 39: Fragmentation Concepts
Highlights many key Internet characteristics
  Decentralized and heterogeneous
    Each network may choose its own MTU
  Connectionless datagram protocol
    Each fragment contains full routing information
    Fragments can travel independently, on different paths
  Best effort network
    Routers/receiver may silently drop fragments
    No requirement to alert the sender
  Most work is done at the endpoints
    i.e. reassembly

## Slide 40: Fragmentation in Reality
Fragmentation is expensive
  Memory and CPU overhead for datagram reconstruction
  Want to avoid fragmentation if possible
MTU discovery protocol
  Send a packet with “don’t fragment” bit set
  Keep decreasing message length until one arrives
  May get “can’t fragment” error from a router, which will explicitly state the supported MTU
Router handling of fragments
  Fast, specialized hardware handles the common case
  Dedicated, general purpose CPU just for handling fragments

## Slide 41: Fragmentation Exercise
MTU = 1200
MTU = 2500
Data
Data
Data
IP Hdr
IP
IP
ID = 123 Length = 2420, M = 0
2400
20
Length = 1196, M = 1,
ID=123, Offset = 0
Length = 1196, M = 1,
ID = 123, Offset = 147
1176
20
1176
20
1176
+ 1176
+ 48
= 2400
Data
IP
Length = 68, M = 0,
ID = 123, Offset = 294
48
20

## Slide 42: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 43: The IPv4 Address Space Crisis
Problem: the IPv4 address space is too small
  232 = 4,294,967,296 possible addresses
  Less than one IP per person
Parts of the world have already run out of addresses
  IANA assigned the last /8 block of addresses in 2011
Region | Regional Internet Registry (RIR) | Exhaustion Date
Asia/Pacific | APNIC | April 19, 2011
Europe/Middle East | RIPE | November 25, 2019
South America | LACNIC | August 21, 2020
North America | ARIN | September 22, 2015
Africa | AFRINIC | January 2022 (Projected)

## Slide 44: IPv6
IPv6, first introduced in 1998
  128-bit addresses
  4.8 * 1028 addresses per person
Address format
  8 groups of 16-bit values, separated by ‘:’
  Leading zeroes in each group may be omitted
  Groups of zeroes can be omitted using ‘::’
  2001:0db8:0000:0000:0000:ff00:0042:8329
  2001:0db8:0:0:0:ff00:42:8329
  2001:0db8::ff00:42:8329

## Slide 45: IPv6 Trivia
Who knows the IP for localhost?
  127.0.0.1
What is localhost in IPv6?
  ::1

## Slide 46: IPv6 Header
Double the size of IPv4 (320 bits vs. 160 bits)
Version
DSCP/ECN
Flow Label
0
8
16
24
31
4
12
19
Datagram Length
Next Header
Hop Limit
Source IP Address
Destination IP Address
Version = 6
Groups packets into flows, used for QoS
Same as IPv4
Same as Protocol in IPv4
Same as TTL in IPv4
Same as IPv4

## Slide 47: Differences from IPv4 Header
Several header fields are missing in IPv6
  Header length – rolled into Next Header field
  Checksum – was useless, so why keep it
  Identifier, Flags, Offset
    IPv6 routers do not support fragmentation
    Hosts are expected to use path MTU discovery
Reflects changing Internet priorities
  Today’s networks are more homogeneous
  Instead, routing cost and complexity dominate
No security vulnerabilities due to IP fragments

## Slide 48: Performance Improvements
No checksums to verify
No need for routers to handle fragmentation
Simplified routing table design
  Address space is huge
  Different role for CIDR
  Standard subnet size is 264 addresses
Simplified auto-configuration
  Neighbor Discovery Protocol
  Used by hosts to determine network ID
  Host ID can be random!

## Slide 49: Deployment Challenges
Switching to IPv6 is a whole-Internet upgrade
  All routers, all hosts
  ICMPv6, DHCPv6, DNSv6
June 2012: 0.2% of global traffic was IPv6; Today ~33%
IPv4
TCP, UDP, ICMP
HTTP, FTP, SMTP, RTP, IMAP, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …

## Slide 50: IPv6 Growth seen from Google
Notes: https://www.google.com/intl/en/ipv6/statistics.html

## Slide 51: Consequences of IPv6
Beware unintended consequences of IPv6
Example: IP blocklists
  Currently, blocklists track IPs of spammers/bots
  Few IPv4 addresses mean list sizes are reasonable
  Hard for spammers/bots to acquire new IPs
Blocklists will not work with IPv6
  Address space is enormous
  Acquiring new IP addresses is trivial

## Slide 52: Additional IPv6 Features
Source Routing
  Host specifies the route to wants packet to take
Mobile IP
  Hosts can take their IP with them to other networks
  Use source routing to direct packets
Privacy Extensions
  Randomly generate host identifiers
  Make it difficult to associate one IP to a host
Jumbograms
  Support for 4Gb datagrams

## Slide 53: Transitioning to IPv6
How do we ease the transition from IPv4 to IPv6?
  Today, most network edges are IPv6 ready
    Windows/OSX/iOS/Android all support IPv6
    Your wireless access point probably supports IPv6
  The Internet core is hard to upgrade
  … but a IPv4 core cannot route IPv6 traffic
Core
Internet
Business
Network
Home
Network
IPv6 Ready
IPv6 Ready
IPv4 Only :(
IPv6 Packets

## Slide 54: Transition Technologies
How do you route IPv6 packets over an IPv4 Internet?
Transition Technologies
  Use tunnels to encapsulate and route IPv6 packets over the IPv4 Internet
  Several different implementations
    6to4
    IPv6 Rapid Deployment (6rd)
    Teredo
    … etc.

## Slide 55: 6to4 Basics
Problem: you’ve been assigned an IPv4 address, but you want an IPv6 address
  Your ISP can’t or won’t give you an IPv6 address
  You can’t just arbitrarily choose an IPv6 address
Solution: construct a 6to4 address
  6to4 addresses always start with 2002::
  Embed the 32-bit IPv4 inside the 128-bit IPv6 address
20 02:
207.
CF 2E:
46.
C0 00:
192.
0000
0
IPv4:
IPv6:

## Slide 56: Routing from 6to4 to 6to4
IPv4
Internet
Dest: 16.79.8.0
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv4 – 16.79.8.0
IPv6 – 2002:104F:0800::
Dest: 2002:104F:0800::
How does a host using 6to4 send a packet to another host using 6to4?

## Slide 57: Routing from 6to4 to Native IPv6
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 192.88.99.1
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 1893:92:13:99::
Special, anycasted IPv4 address for
6to4 Relay Routers
Many ISPs provide 6to4 relay routers

## Slide 58: Routing from Native IPv6 to 6to4
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 207.46.192.0
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 2002:CF2E:C000::
Use normal IPv6 routing to reach a 6to4 relay router

## Slide 59: Problems with 6to4
Uniformity
  Not all ISPs have deployed 6to4 relays
Quality of service
  Third-party 6to4 relays are available
  …but, they may be overloaded or unreliable
Reachability
  6to4 doesn’t work if you are behind a NAT
Possible solutions
  IPv6 Rapid Deployment (6rd)
    Each ISP sets up relays for its customers
    Does not leverage the 2002:: address space
  Teredo
    Tunnels IPv6 packets through UDP/IPv4 tunnels
    Can tunnel through NATs, but requires special relays

## Slide 60: What transition technologies do we see today?
Why?
Widespread prevalence of dual stacks

## Slide 61: CS 4700 / 5700 Network Fundamentals
Transport Layer
(UDP, but mostly TCP)
Revised 2/20/24

## Slide 62: Transport Layer
Why does the Transport Layer exist
UDP and TCP Sockets Semantics
Reading a socket: recv semantics
Resources

## Slide 63: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived “connections”
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 64: Outline
UDP
TCP
  Header Format, Semantics
  Connection Lifecycle, Sequence Numbers
  Error Detection and Recovery
  TCP Options

## Slide 65: The Case for Multiplexing
Datagram network
  No circuits
  No connections
Clients run many applications at the same time
  Who to deliver packets to?
IP header “protocol” field
  8 bits = 256 concurrent streams
Insert Transport Layer to handle demultiplexing
Packet
Network
Data Link
Physical
Transport

## Slide 66: Demultiplexing Traffic
Endpoints identified by <src_ip, src_port, dest_ip, dest_port>
Network
Transport
Application
P1
P2
P3
P4
P6
P7
P5
Host 1
Host 2
Host 3
Unique port for each application
Applications share the same network
Server applications communicate with multiple clients

## Slide 67: Layering
Application
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Lowest level end-to-end protocol (in theory)
  Transport header only read by source and destination
  Routers view transport header as payload
Application
Transport
Network
Data Link
Physical
Network
Data Link
Layers communicate peer-to-peer

## Slide 68: User Datagram Protocol (UDP)
Simple, connectionless datagram
  C sockets: SOCK_DGRAM
Port numbers enable demultiplexing
  16 bits = 65535 possible ports
  Port 0 is invalid
Checksum for error detection
  Detects (some) corrupt packets
  Does not detect dropped, duplicated, or reordered packets
Destination Port
0
16
31
Payload Length
Source Port
Checksum

## Slide 69: Usage Example (Python)
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
sock.sendto(“message”, (“127.0.0.1”, 3456))
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
sock.bind((“127.0.0.1”, 3456))
data, addr = sock.recvfrom(2048)
Sending on a client socket
Receiving on a server socket
No “connection”, UDP sockets are mostly stateless.
One UDP socket may send to many destinations.
OS needs to be told what port this application is listening to
One UDP socket may receive from multiple destinations

## Slide 70: UDP Socket Semantics
sock.sendto(msg1, destination)
sock.sendto(msg2, destination)
sock.sendto(msg3, destination)
Src Prt
Dst Prt
msg1
Src Prt
Dst Prt
msg2
Src Prt
Dst Prt
msg3
Sending
Receiving
data, addr = sock.recvfrom(2048) #msg1
data, addr = sock.recvfrom(2048) #msg2
data, addr = sock.recvfrom(2048) #msg3
UDP Header
Datagram 1:
Datagram 2:
Datagram 3:

## Slide 71: UDP Socket Semantics
Sending a buffer will produce exactly one datagram containing the data from the buffer
  Warning: UDP datagrams may hold up to 65,000 bytes of data…
  If len(UDP datagram) > MTU, IP will need to fragment it
Receiving will return exactly one, full datagram
  Not a partial datagram, not >1 datagrams

## Slide 72: Uses for UDP
Invented after TCP
  Why?
Not all applications can tolerate TCP
Custom protocols can be built on top of UDP
  Reliability? Strict ordering?
  Flow control? Congestion control?
Examples
  RTMP – real-time media streaming (e.g. voice, video)
  uTP – “microtransport” protocol used by BitTorrent
  QUIC – app-level transport protocol developed by Google to speed up HTTP

## Slide 73: Outline
UDP
TCP
  Header Format, Semantics
  Connection Lifecycle, Sequence Numbers
  Error Detection and Recovery
  TCP Options

## Slide 74: Transmission Control Protocol
Options
Reliable, in-order, bi-directional byte streams
  Port numbers for demultiplexing
  Virtual circuits (connections)
  Flow control
  Congestion control, approximate fairness
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 75: TCP Header Fields
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen
Used to detect out of order, duplicate, and missing packets
Header length. Default length is 20 bytes, but may be longer with options.
Not used.
Used for flow control (protecting the receiver from overloading)
Used for connection establishment (SYN), acknowledgement (ACK), connection close (FIN), and errors (RST).

## Slide 76: Usage Example
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
sock.connect((“127.0.0.1”, 3456))
sock.sendall(“message”)
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
sock.bind((“127.0.0.1”, 3456))
sock.listen()
conn, addr = sock.accept()
data = conn.recv(2048)
Sending on a client socket
Receiving on a server socket
TCP is stateful, connections must be formed
One TCP socket only sends over one connection
OS needs to be told what port this application is listening to
Socket “listens” for incoming connections
Accept spawns a second socket

## Slide 77: TCP Socket Semantics
sock.send(msg1)
sock.send(msg2)
sock.send(msg3)
Src Prt
Dst Prt
msg1
Src Prt
Dst Prt
msg2
Src Prt
Dst Prt
msg3
Sending
TCP Header
Segment 1:
Segment 2:
Segment 3:
Src Prt
Dst Prt
msg1 + msg2 + msg3
Segment 1:
Src Prt
Dst Prt
msg1 + msg2a
Src Prt
Dst Prt
msg2b + msg3
Segment 1:
Segment 2:

## Slide 78: TCP Socket Semantics
sock.send(msg1)
sock.send(msg2)
sock.send(msg3)
msg1
msg2
msg3
Sending
Receiving
data = sock.recv(2048)

## Slide 79: TCP Socket Semantics
Sending a buffer may produce any number of segments
  In practice, TCP tries to optimize by putting close to 1460 bytes in each segment
  But this is not true under all circumstances
Receiving may return any number of data bytes
  Could return part of a segment…
  Or a full segment…
  Or multiple segments…

## Slide 80: send* semantics
send(bytes), sendto(bytes, addr): send data bytes to the socket
TCP
  Multiple TCP segments sent depending number of bytes and max size packet in the Data Link, e.g., Ethernet max size is 1500 bytes less headers for IP and TCP
UDP
  A single datagram is sent at one time up to bytes long (up to 65535 bytes → BEWARE MAX ethernet packet size only holds 1472 bytes)
  No guarantee a sent datagram will be delivered

## Slide 81: recv* semantics
Socket semantics are somewhat similar to File I/O semantics
recv(size), recvfrom(size): size = maximum amount of data that can be read at once
TCP
  No guarantee to receive all the data sent in a single read, but all data will arrive
UDP
  A single datagram is read at one time (up to 65535 bytes → BEWARE MAX ethernet packet size only holds 1472 bytes)
  No guarantee a sent datagram will be received

## Slide 82: Asynchronous communication
recv() is a blocking call
  It waits until the socket has something to read
  If nothing is there, it waits forever
OK if the communication is synchronous
  client sends, server responds, client sends, server responds, …
But what is the client doesn’t know when the message will arrive or needs to read multiple open sockets or look for multiple messages
More on this on Friday

## Slide 83: UDP sockets are naturally asynchronous
UDP sockets `bind` to a port, NOT to (address, port)
UDP ‘bind’ delivers packets from any host sending to the port
Challenge: what is the source IP address and port of the sending host?
  Does the app care about this packet from this host
`revcfrom()` returns the data and the source IP and port of the sender
`sendto(data, address)’ does the for sending
  address is (dest_IPaddr, dest_port)

## Slide 84: Idleness, or how to get more work from the server
Recall, recv*() is a blocking call
If messages are not arriving frequently, the code is blocked from continuing
  App goes idle
  Can impact performance
Commonly addressed by:
  Using `select()` or `poll()`; single threaded solutions
    MUCH simpler to reason and debug
    Performance lower than tuned threaded solutions
  Threading
    MUCH MORE complicated to debug
    MUCH higher performance when Tuned CORRECTLY

## Slide 85: For our next class:
Review the material(s) on the schedule for Week 3

## Slide 86
Examples in Python

## Slide 87: Resources & examples — all on the course website
The web has tons of examples. If the one’s below don’t work for you, look for others.
C
  Beej’s Guide to Network Programming: https://beej.us/guide/bgnet/html/
  TCP echo server example: https://www.geeksforgeeks.org/tcp-server-client-implementation-in-c/
  UDP echo server example: https://www.geeksforgeeks.org/udp-client-server-using-connect-c-implementation/
Python
  Socket Programming HOWTO: https://docs.python.org/3/howto/sockets.html
  TCP echo server (1st example): https://docs.python.org/3/library/socket.html#example
  UDP echo server (nice design, but needs to be converted to Python3): https://svn.python.org/projects/python/trunk/Demo/sockets/udpecho.py
Java
  Distributed Systems text: Chapters 3 and 4
  TCP echo server: https://www.geeksforgeeks.org/socket-programming-in-java/
  UDP echo server: https://www.baeldung.com/udp-in-java , https://www.geeksforgeeks.org/working-udp-datagramsockets-java/

## Slide 88: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 89: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence and acknowledgement numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 90: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number (+1)
  Sequence # must increment on receiving a SYN
Client
Server
<SYN, Seq # C, Ack # ?>
<SYN/ACK, Seq # S, Ack # C+1>
<ACK, Seq # C+1, Ack # S+1>
Seq #
Ack#
Seq #
Ack #
C
?
S
C
C+1
S
S+1
C+1
Why
Sequence # +1?
Notes: 211

## Slide 91: Why Random Initial Sequence Numbers?
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Preventing packet injection
  How Kevin Mitnick hacked into the SDSC
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood is a common denial of service attack
  Solution: SYN cookies

## Slide 92: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 93: Data Transfer
TCP uses a byte stream abstraction
  Initial, random values selected during setup
  Each byte in each stream is numbered
  32-bit value, wraps around
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS, typically 1460 bytes)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550
Byte stream to send

## Slide 94: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
<Seq # 7, Ack # 23> 1460 data bytes
<ACK, Seq # 23, Ack # 1467> 730 data bytes
<ACK, Seq # 1467, Ack # 753> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
1467
753
753
2927
23
7
<ACK, Seq # 753, Ack # 2927> 240 data bytes
2927
993
Data and ACK in the same packet
Problem: this depicts a stop-and-wait protocol
Will not be able to utilize all available bandwidth

## Slide 95: Review from Layer 2: Stop and Wait Protocol
Simplest form of reliability
  Example: Bluetooth
Problems?
  Low utilization: can only have one segment in flight at any time
10Gbps link and 10ms delay
  Need 100 Mb to fill the pipe
  Assume packets are 1500B
1500B * (8b/1B) / 2 = 6000b = 0.006Mb
Utilization is 0.006%
Sender
Receiver
Segment
ACK
Timeout
Segment
Timeout
Retransmit Segment
Notes: 10ms is one-way delay.
Assume path is symmetrical. 2*10ms is round trip time.
Can only send next packet after ACK is received.

## Slide 96: Review from Layer 2: Sliding Window
Allow multiple outstanding, un-ACKed segments
Number of un-ACKed segments is called the window
Sender
Receiver
Segments
ACKs
Window
Made famous by TCP

## Slide 97: Flow Control
Problem: how big should the window be?
  Too many packets may overwhelm the receiver
  Size of the receiver's buffers may change over time
Solution: advertised window
  Receiver tells the sender how big their buffer (the window) is
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Advertised window may go to zero!

## Slide 98: Flow Control: View from the Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
sock.send()
Must be buffered until ACKed
Buffer of Bytes to Send
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 99
Sliding Window Example
Buffer of Bytes to Send
Window = 3* MSS
Client
Server
<Seq # 7> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
2927
23
7
1460
1460
1460
1460
1460
1460
1460
<Seq # 1467> 1460 data bytes
<Seq # 2927> 1460 data bytes
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 2927>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387> 1460 data bytes
<Seq # 5847> 1460 data bytes
<Seq # 7307> 1460 data bytes
1467
23
2927
23
4387
23

## Slide 100: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension

## Slide 101: Sequence Numbers, Revisited
32 bits, unsigned
  Why so big?
To avoid acknowledgement ambiguity in the window you need…
  |Sequence # Space| > 2 * |Sending Window Size|
  232 > 2 * 216

## Slide 102
Ambiguous Window Example
Client
<Seq # 0>
<Seq # 1>
<Seq # 0>
<ACK, Ack # 0>
Imagine that sequence numbers are 1-bit
  Segments are numbered zero or one
Assume window size = 3 segments
Which segment was acknowledged?

## Slide 103: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 104: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
  shutdown()
Acknowledge the last FIN
  Sequence number + 1
Client
Server
<FIN, Seq # X, Ack # Y>
<ACK, Seq # Y, Ack # X+1>
<ACK, …>
<…> Data
<FIN, Seq # Z, Ack # X+1>
<ACK, Seq # X+1, Ack # Z+1>

## Slide 105: Error Detection and Recovery in TCP

## Slide 106: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped

## Slide 107
Out-of-Order (OoO) Delivery Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 1467>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387>
<Seq # 5847>
<Seq # 7307>
1467
23
1467
23
4387
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Windows does not slide, no transmission
Ack # catches up by two segments
Window slides by two segments

## Slide 108
Packet Loss Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Windows does not slide, no transmission
<ACK, Ack # 1467>
1467
23

## Slide 109
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
<ACK, Ack # 1467>
1467
23
<Seq # 1467>
23
5847
5847
23
Window slides by three segments
Timeout, retransmit
<Seq # 2927>
<Seq # 4387>
<ACK, Ack # 5847>

## Slide 110: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
Lost segments detected by sender
  Use timeout to detect lost segments and missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 111: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 112: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
RTT Sample

## Slide 113: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 114: TCP Options

## Slide 115: Common TCP Options
Window scaling
Timestamp
SACK: selective acknowledgement
Maximum segment size (MSS)
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 116: Utilization, Revisited
Sequence numbers are 32 bits, advertised windows are 16 bits
  The most data that can be in flight in parallel is 2^16 bytes
Recall that link capacity is measured by the bandwidth delay product
  bandwidth * delay = capacity
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^16 bytes / 100 ms ~ 5 Kbps
  500 ms of delay  2^16 bytes / 500 ms ~ 1 Kbps
But ethernet scales to 1 Gbps, 10 Gbps, 100 Gbps…

## Slide 117: Window Scaling
Problem: the advertised window is only 16-bits
  Effectively caps the window at 65536 bytes, 64 KB
Solution: introduce a window scaling value
  scaled_adv_wnd = adv_wnd << wnd_scale;
  Maximum shift is 14 bits, 1GB maximum window

## Slide 118: Sequence Number Scaling
Problem: sequence numbers are only 32 bits
  Effectively caps the window at 2^32 ~ 4 GB
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^32 bytes / 100 ms ~ 344 Mbps
  500 ms of delay  2^32 bytes / 500 ms ~ 69 Mbps
Solution: the PAWS algorithm
  32-bit timestamp option in TCP header
  When was the packet sent (approximately)
  Effectively extends the sequence numbers space to 64 bits

## Slide 119: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
4
4
5
6
7
4
4
4
4

## Slide 120: Other Common Options
Maximum segment size (MSS)
  Essentially, what is the hosts MTU
  Saves on path discovery overhead

## Slide 121: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 122: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence and acknowledgement numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 123: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number (+1)
  Sequence # must increment on receiving a SYN
Client
Server
<SYN, Seq # C, Ack # ?>
<SYN/ACK, Seq # S, Ack # C+1>
<ACK, Seq # C+1, Ack # S+1>
Seq #
Ack#
Seq #
Ack #
C
?
S
C
C+1
S
S+1
C+1
Why
Sequence # +1?
Notes: 211

## Slide 124: Why Random Initial Sequence Numbers?
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Preventing packet injection
  How Kevin Mitnick hacked into the SDSC
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood is a common denial of service attack
  Solution: SYN cookies

## Slide 125: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 126: Data Transfer
TCP uses a byte stream abstraction
  Initial, random values selected during setup
  Each byte in each stream is numbered
  32-bit value, wraps around
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS, typically 1460 bytes)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550
Byte stream to send

## Slide 127: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
<Seq # 7, Ack # 23> 1460 data bytes
<ACK, Seq # 23, Ack # 1467> 730 data bytes
<ACK, Seq # 1467, Ack # 753> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
1467
753
753
2927
23
7
<ACK, Seq # 753, Ack # 2927> 240 data bytes
2927
993
Data and ACK in the same packet
Problem: this depicts a stop-and-wait protocol
Will not be able to utilize all available bandwidth

## Slide 128: Review from Layer 2: Stop and Wait Protocol
Simplest form of reliability
  Example: Bluetooth
Problems?
  Low utilization: can only have one segment in flight at any time
10Gbps link and 10ms delay
  Need 100 Mb to fill the pipe
  Assume packets are 1500B
1500B * (8b/1B) / 2 = 6000b = 0.006Mb
Utilization is 0.006%
Sender
Receiver
Segment
ACK
Timeout
Segment
Timeout
Retransmit Segment
Notes: 10ms is one-way delay.
Assume path is symmetrical. 2*10ms is round trip time.
Can only send next packet after ACK is received.

## Slide 129: Review from Layer 2: Sliding Window
Allow multiple outstanding, un-ACKed segments
Number of un-ACKed segments is called the window
Sender
Receiver
Segments
ACKs
Window
Made famous by TCP

## Slide 130: Flow Control
Problem: how big should the window be?
  Too many packets may overwhelm the receiver
  Size of the receiver's buffers may change over time
Solution: advertised window
  Receiver tells the sender how big their buffer (the window) is
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Advertised window may go to zero!

## Slide 131: Flow Control: View from the Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
sock.send()
Must be buffered until ACKed
Buffer of Bytes to Send
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 132
Sliding Window Example
Buffer of Bytes to Send
Window = 3* MSS
Client
Server
<Seq # 7> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
2927
23
7
1460
1460
1460
1460
1460
1460
1460
<Seq # 1467> 1460 data bytes
<Seq # 2927> 1460 data bytes
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 2927>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387> 1460 data bytes
<Seq # 5847> 1460 data bytes
<Seq # 7307> 1460 data bytes
1467
23
2927
23
4387
23

## Slide 133: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension

## Slide 134: Sequence Numbers, Revisited
32 bits, unsigned
  Why so big?
To avoid acknowledgement ambiguity in the window you need…
  |Sequence # Space| > 2 * |Sending Window Size|
  232 > 2 * 216

## Slide 135
Ambiguous Window Example
Client
<Seq # 0>
<Seq # 1>
<Seq # 0>
<ACK, Ack # 0>
Imagine that sequence numbers are 1-bit
  Segments are numbered zero or one
Assume window size = 3 segments
Which segment was acknowledged?

## Slide 136: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 137: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
  shutdown()
Acknowledge the last FIN
  Sequence number + 1
Client
Server
<FIN, Seq # X, Ack # Y>
<ACK, Seq # Y, Ack # X+1>
<ACK, …>
<…> Data
<FIN, Seq # Z, Ack # X+1>
<ACK, Seq # X+1, Ack # Z+1>

## Slide 138: Error Detection and Recovery in TCP

## Slide 139: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped

## Slide 140
Out-of-Order (OoO) Delivery Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 1467>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387>
<Seq # 5847>
<Seq # 7307>
1467
23
1467
23
4387
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Windows does not slide, no transmission
Ack # catches up by two segments
Window slides by two segments

## Slide 141
Packet Loss Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Windows does not slide, no transmission
<ACK, Ack # 1467>
1467
23

## Slide 142
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
<ACK, Ack # 1467>
1467
23
<Seq # 1467>
23
5847
5847
23
Window slides by three segments
Timeout, retransmit
<Seq # 2927>
<Seq # 4387>
<ACK, Ack # 5847>

## Slide 143: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
Lost segments detected by sender
  Use timeout to detect lost segments and missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 144: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 145: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
RTT Sample

## Slide 146: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 147: TCP Options

## Slide 148: Common TCP Options
Window scaling
Timestamp
SACK: selective acknowledgement
Maximum segment size (MSS)
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 149: Utilization, Revisited
Sequence numbers are 32 bits, advertised windows are 16 bits
  The most data that can be in flight in parallel is 2^16 bytes
Recall that link capacity is measured by the bandwidth delay product
  bandwidth * delay = capacity
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^16 bytes / 100 ms ~ 5 Kbps
  500 ms of delay  2^16 bytes / 500 ms ~ 1 Kbps
But ethernet scales to 1 Gbps, 10 Gbps, 100 Gbps…

## Slide 150: Window Scaling
Problem: the advertised window is only 16-bits
  Effectively caps the window at 65536 bytes, 64 KB
Solution: introduce a window scaling value
  scaled_adv_wnd = adv_wnd << wnd_scale;
  Maximum shift is 14 bits, 1GB maximum window

## Slide 151: Sequence Number Scaling
Problem: sequence numbers are only 32 bits
  Effectively caps the window at 2^32 ~ 4 GB
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^32 bytes / 100 ms ~ 344 Mbps
  500 ms of delay  2^32 bytes / 500 ms ~ 69 Mbps
Solution: the PAWS algorithm
  32-bit timestamp option in TCP header
  When was the packet sent (approximately)
  Effectively extends the sequence numbers space to 64 bits

## Slide 152: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
4
4
5
6
7
4
4
4
4

## Slide 153: Other Common Options
Maximum segment size (MSS)
  Essentially, what is the hosts MTU
  Saves on path discovery overhead